Firmware operations in DGS

JTA 20240222

# Introduction
The method of maintaining firmware using Tim Madden’s Java applet is now completely deprecated and is no longer supported by the VME IOCs. Do not use this method any more.
Maintenance of the firmware is now performed using three console functions directly entered at the terminal window of any IOC, named EraseFlash(), ProgramFlash(), and VerifyFlash(). These functions are entered using the terminal window.. Remember that the terminal window does not understand the Backspace key; you must use Ctrl-H.
# Board numbers and slots
Each “.cmd” file read by the VME IOC assigns board numbers at boot, such as shown here.

asynDigitizerConfig("MDIG1",0,2)
asynTrigRouterConfig1("RTR4",4,7)
asynTrigMasterConfig1("MTRG",5,6)
In each case the textual argument is the name of the module, the second argument is the board number and the third argument is the slot in the VME crate where the module resides.
# EraseFlash(<bdnum>,<flashsection>)
The EraseFlash() function requires as its first argument the board number assigned by the IOC at boot. The second number is which half of the flash RAM is to be used. All modules use the lower half at power-up, so the <flashsection> should always be zero.
As EraseFlash() runs it will count off the addresses within the flash memory that are being erased and tell you how many times each block had to be polled after issuing the erase command. Under normal circumstances this is just to let you know it’s working. If the poll count is very high (>200) this may indicate that the flash memory chip is nearing the end of its lifetime and the module may need to be repaired in the near future.
# ProgramFlash(<bdnum>,<flashsection>,”<filename>”)
The ProgramFlash() function requires as its first argument the board number assigned by the IOC at boot. The second number is which half of the flash RAM is to be used. All modules use the lower half at power-up, so the <flashsection> should always be zero.
ProgramFlash() automatically calls ErashFlash() before programming, because that’s how flash memory works. So you don’t have to do EraseFlash() manually, but sometimes we will manually erase it just to check the poll count values if we think the flash memory chip is getting old.
The file argument is the full path on the file server, something like
/dk/fs2/dgs/global_32/ioc/FW_Maint/trigger_top.bin
We keep the firmware images we believe to be the correct ones for DGS in that folder. However, the real place the firmware images are stored is on the Subversion repository. Subversion is the “golden copy”.
# VerifyFlash(<bdnum>,<flashsection>,”<filename>”)
The verify function will read the flash memory and compare it to the data in the file. It will count off addresses every so often just so that you know it’s working. There may be a few mismatches at the very end, this is acceptable so long as
- the mismatches are at the very, very end
- there are no more than 16 or so
this situation is caused by the way the data must be ‘chunked’ into buffers, and is caused by a mismatch between values of 0 and 0xFFFFFFFF. Empty flash memory may read either depending upon which block is the end one, so this varies based upon the size of the program for the different FPGAs.
If there’s a real problem, you’ll see thousands of mismatches from the start.